## Slide 1
2025
The Power couple = Flow + Probe data
Combining performance metrics & flow data for optimal network insights

## Slide 2
Challenge: Monitor 20 ingress (transit) points

## Slide 3
How ISPs monitor today?
Hosting Provider
There are three solutions

## Slide 4
Probes placed at external hosting locations
Inbound path is probabilistic (BGP decision outside operator’s control)
Require many vantage points (~50) to establish coverage
Operator-managed external probes
Ingress 2 (TATA SIN2)
Ingress 3 (Airtel BOM1)
Hosting provider-2
Hosting provider-1
Hosting provider-3
Ingress 1 (RETN LDN1)
Other ingress points
Probes placed at
various locations
Central Endpoint

## Slide 5
Third-party probe dataset providers
Subscription based access to large probe pools
Global coverage from vendor’s vantage network
Still probabilistic for inbound transit paths
Regional ISP coverage questionable
Ingress 2 (TATA SIN2)
Ingress 1 (RETN LDN1)
Central Endpoint
probe dataset provider
Ingress 3 (Airtel BOM1)
Other ingress points

## Slide 6
Deterministic path selection via BGP announcements to a test host
Use 2 probes and announce a dedicated IPv6 /48 at each transit.
Each /48 is announced only via one ingress, enabling deterministic path validation to a single test host.
This setup allows broad, scalable ingress monitoring — with static per-transit routing.
Central Endpoint
Probe 1
Probe 2
2001:db8:1::/48
2001:db8:2::/48
2001:db8:3::/48
2001:db8:14::/48
IP:s from: 2001:db8:0::/40
Ingress 1 (RETN LDN1)
Ingress 2 (TATA SIN2)
Ingress 3 (Airtel BOM1)
Other ingress points

## Slide 7: Comparison of three solutions
Metric | Solution 1 | Solution 2 | Solution 3
Probe Location | External hosting (self-managed) | Vendor vantage network | 2 on-premises probes
Path Control | Low / probabilistic inbound | Low / probabilistic inbound | High - deterministic via /48 per transit
Hardware Cost | Medium–High | None | Low
Ongoing Cost | VPS hosting + maintenance | Subscription fees | Minimal OPEX
Deployment Complexity | High | Low | Low
Coverage | Geographic spread improves odds | Vendor coverage improves odds | Full ingress coverage by design
Independence | High (you own probes) | Low (vendor dependency) | High

## Slide 8: Limitations of probe only monitoring
High deployment & maintenance cost Installing and managing probes at every ingress point increases hardware, provisioning, and troubleshooting workload.
Complex test orchestration Synthetic tests must be manually configured per transit provider using static routing or BGP tweaks.
Doesn’t scale efficiently As transit links grow, testing complexity and monitoring overhead increase exponentially.
Inflexible to change Adding/removing a provider means reconfiguring test logic often manually.
Blind spots remain If routing policies shift or a transit isn’t actively preferred, visibility through that ingress can disappear.
Notes: we’ve summarized the core limitations of this method.
“First, it’s expensive and hardware-intensive. You’re looking at 20+ probes for full coverage.”
“Second, orchestrating synthetic tests per ingress is technically complex and error-prone.”
“Third, it doesn’t scale well. As you add more transit links, your monitoring matrix grows exponentially.”
“And finally, you may completely miss an underperforming path if no real traffic or tests happen to go that way.”
[Close – Tease the alternative]
“So while this model is widely used, it’s heavy, costly, and hard to maintain. And that’s exactly why we propose a radically simpler, smarter approach — using just two probes and a dedicated IPv6 prefix. I’ll show you how that works next.”

## Slide 9
Looking Glass
Flow Explorer
Capacity Planner
SNMP
BGP
IS-IS
DNS
Netflow
OSPF
Telemetry
BENOCS CORE ENGINE
PROTOCOL POOL
PROCESSING
NETWORK INTELLIGENCE
Our proprietary aggregation and cross correlation process requires significantly less compute power compared to competitors
CDN Flow Director
Anomaly Detection
Application Monitor
What BENOCS does:
Notes: "Some of you might have heard of us, but for those who haven’t, let me introduce BENOCS. We specialize in providing network intelligence solutions to different departments such as Peering, Network operation centers, Capacity planning and Network Engineering. Our mission is to help you gain comprehensive visibility of the traffic flowing through your network, from its origin to termination.
At BENOCS, we offer more than just a product; we also provide consultation and support to help you manage your network more efficiently and effectively. In a recent conversation with a customer, we uncovered some fascinating insights that we believed would be valuable to share in a forum like this.

## Slide 10: How BENOCS correlates?
1
Probe metrics
Performance data from strategic network points provides detailed metrics on latency, packet loss and jitter.
2
Flow records
Flow analytics capture network-wide traffic statistics revealing source, handover, ingress and egress regions, volume and application data
3
BENOCS Core
Our core engine automatically links performance issues to specific traffic flows, providing complete context for every alert

## Slide 11
Step 1: Anomaly in the probe data
Notes: Solution: Use generic alert system with a) thresholds (good enough) b) anomaly detection (reduces noise)

## Slide 12
Step 1: Alert triggered
https://xyz.com/asflows?asFilters=%7B%22HND%22%3A%5B%221299%22%5D%2C%22INROUTER%22%3A%5B%22LDN1%22%5D%7D&customDimension=%22AS_APPLICATION%2CAS_SRC_INGRESS%2CAS_HND_INGRESS%2CROUTER_IN_INGRESS%2CROUTER_OUT_INGRESS%2CAS_NXT_INGRESS%2CAS_DST_INGRESS%22&dateRange=LAST_7_DAYS&disaggregations=%7B%7D&tagAggregations=%5B%7B%22dimension%22%3A%22ROUTER_OUT_INGRESS%22%2C%22id%22%3A4%7D%5D&tags=%5B%5D&tsDimension=AS_APPLICATION
Peer and ingress router are known from the IPv6 prefix
  That gives us the key identifiers to correlate with flow data
  All traffic of the alerted ingress-point can be displayed to show full context

## Slide 13
Step 2: Flow correlation
Traffic on the affected ingress point was jammed by Steam/Valve traffic
LDN1

## Slide 14
Step 3 : Detailed investigation
Additional traffic on the affected ingress point was mainly targeted at region 5

## Slide 15: Real-world impact: Steam traffic
Steam hit 40,270,997 concurrent users on Feb 28, 2025, due to the massive popularity of Black Myth: Wukong which triggered multi Tbps bursts at provider ingress points
1
2
3
4
Anomaly alert triggered
Performance degradation detected at key ingress points
Flow Correlation
BENOCS instantly identified the traffic pattern and source
Detailed Investigation
Valve's content distribution automatically pinpointed, and the affected region spotted
Resolution
Traffic rerouted within minutes instead of hours

## Slide 16: Power couple = Flow + Probe data
Probe  fault detection
Reveals performance issues such as Latency, Jitter but misses broader traffic context
Flow  Full context & Scope
Shows traffic statistics such as volume, ingress and egress specific traffic and the applications
Combined full visibility
Delivers true end-to-end visibility with both performance precision and traffic context

## Slide 17: Recommendations for ISPs
1. Strengthen Network Capacity
Upgrade backbone bandwidth and core hardware
Distribute load across multiple PoPs/data centres
2. Improve Content Delivery
Peer directly with major platforms or IXPs
Host content locally via CDNs/caching partnerships
Coordinate with providers to pre-load updates
3. Optimize Traffic Flow
Prioritize gaming/streaming traffic during peaks
Use real-time monitoring and analytics
4. Enhance End-User Experience
Offer setup guides for optimal connectivity

## Slide 18
Péter György pgyoergy@benocs.com
Thank you!
BENOCS GmbH
Reuchlinstr. 10, 10553 Berlin
+49 30 577 000 4 – 0
benocs.com
18
Questions?