## Slide 1: Defending the Realm: DDoS detection and mitigation
José Alberto Nistal
BalticNOG – September XX, 2025
DRAFT

## Slide 2
DDoS traffic and attack trends - 2024
Nokia Threat Intelligence Report 2024
DNS
#1 vector
36% of attacks
Botnets
1M active bots
60% of attacks use < 100 bots
Residential Proxy abuse
Leveraging Millions of residential IP’s in “free” VPN services
Duration
44% lasts
< 5 minutes
But higher frequency
AI & automation
Driving faster morphing attacks
New
Carpet bombing
on the rise
13% to 256+ IPs
2.8% to >1K IPs
Largest: 16K IPs

## Slide 3
How do legacy DDoS tools detect DDoS?
Traffic is good… until it isn’t
Other DDoS tools use Flow based traffic thresholds to trigger DDoS events.
Traffic is good until it crosses some configured threshold, and then it’s suddenly bad.
Ok, so what’s the big deal?
  Flows are only identified as DDoS once an object is configured for detection, thresholds are set, and thresholds are exceeded
  Operators must maintain thresholds and configuration for every type of DDoS misuse out on the Internet
  Hard to maintain, very inaccurate
time
DDoS threshold
bps/pps
Good
Bad

## Slide 4
How do you need your DDoS tool to be today?
1 | Automated
2 | Lightning-fast
3 | At scale

## Slide 5
Deepfield Defender

## Slide 6
A high-scalable software platform that combines
Nokia Deepfield Genome® - a big data based Supply-Chain and Security map of the Internet
Telemetry from your routers
to provide DDoS protection
On-prem Deepfield Defender
Genome® feed
Telemetry
Nokia Deepfield cloud
Security Operations/ Network Operations
DDoS alerting
Your
IP network
Internet
Transit
Peering
1
2
Mitigation
Deepfield Defender in a nutshell
Notes: Honey pots

## Slide 7
1. Automated
The Secure Genome Advantage
Massive real world sample library + Genome detection rules + Genome Tags = automated DDoS detection for all traffic
Deepfield Secure Genome™
Automated
Protection

## Slide 8
What does automated detection mean?
No need to configure or maintain thresholds → Simplified operations, improved accuracy & reliability
Immediate detection from day one → Quick initial setup & easy onboarding for new customers
Detection covers all traffic, including non-protected customers → Create opportunities to upsell protection services

## Slide 9
2. Lightning-fast
Sampled Port Mirroring (SPM)
Zero cache
Real-time DDoS detection
Header + payload telemetry: TCP SEQ & ACK numbers, DNS queries, etc.
Available on Nokia SR & Juniper MX routers
DDoS traffic
Internet
Traditional Flow (~30-60s, IP header only)
SPM (<1s, IP header + payload)
Router
Deepfield

## Slide 10
*config mirror
mirror-dest 9999 name "SAMPLED-MIRROR" create
slice-size 128
sampling-rate 2000
encap
layer-3-encap ip-udp-shim-sampled create
gateway create
ip src 10.10.10.4 dest 172.16.201.120
udp src 9000 dest 5309
exit
exit
exit
no shutdown
exit
mirror-source 9999 name "SAMPLED-MIRROR"
port lag-4 ingress
sap lag-2:235 ingress
no shutdown
exit
SPM in detail
Mirror ingress traffic samples, 1st slice only
1:2000 sampling rate
First 128 bytes of packet
Forward with zero delay to Deepfield
SROS: over UDP tunnel with shim-header (includes drop/forwarding stats + interface info)
Juniper MX: over GRE tunnel (no shim header – requires Netflow for reporting dropped traffic)
Supported routers:
Nokia: FP4/FP5 rtr with SROS20.7R1 or later
Juniper: JunOS 19.4 or later
Mirrored BW: typically < 0.02% of monitored BW
With sampling rate 1:1-2000, slice-size 128:
  100 Gbps traffic → <20 Mbps
Internet peering links to be monitored
Notes: JunOS configuration: see Documentation: Router Configuration Examples — Deepfield Customer Documentation documentation

## Slide 12
Mitigation Compiler Engine (MCE):
ML engine that compiles optimal surgical filter-list for each attack
Filter match criteria for surgical filters:
Filter installation using Netconf or BGP FlowSpec
Other supported mitigation Options:
  RTBH
  BGP or FlowSPec divert to on-net scrubber
  Attack advertisement to cloud-DDoS service
multi-vector amplification
Carpet bomb
TCP SA
reflection
botnet + spoofed TCP
FP4/FP5 ASIC is purpose-built to filter at Tbps line-rate!
dst/src IP match-lists
dst/src Port
Protocol
Packet length
Fragment
TCP flags
TTL
Mitigate the attack using the most efficient strategy
Notes: Why pay $$$ for server cards to apply long lists of filters, while Router ASIC is built to do this at much higher scale?

## Slide 13
Off-ramp to Defender Mitigation System (DMS)
Edge router-based mitigation
Peering gateway
IP core
Off-ramp approach: Deploy dedicated DMS for off-ramp, terabit-level DDoS mitigation.
7750
DMS-1
Mitigation at the edge:
Use existing routers to drop DDoS traffic at the edge.
Deepfield DDoS mitigation – implementation options
Both options can be combined

## Slide 14
3. At scale
Nokia Service Routers
Large filter-scale: 256K filter-entries
Predictable terabit-scale performance: surgical filtering, without impacting Router-scaling and performance
Fast programming of filters
Purpose-built DDoS mitigation appliance for offramp scrubbing
  FP5 powered with Advanced Countermeasures Engine
  Optimized SROS software variant for DDoS mitigation (only)
2.8 Tbps mitigation capacity
  24 x QFSP-DD ports supporting 10G/40G/100G/800G per port
  with Nx100Gbps Pay-as-You-Go licenses
Fully Managed and controlled by Deepfield Defender
7750 DMS-1-24D
Deepfield Defender Mitigation System (DMS)

## Slide 15
Mitigation filters visible in UI
Notes: We will also monitor the Deepfield Defender console which lists all ongoing and past DDoS events. When the attack is detected, the event count will turn red and a new DDoS incident entry will be added in the console.

## Slide 16
How do you need your DDoS tool to be today?
1 | Automated
 | Secure Genome
2 | Lightning-fast
 | Sampled Port Mirroring
3 | At scale
 | FP5 (edge/DMS)

## Slide 18
Copyright and confidentiality
The contents of this document are proprietary and confidential property of Nokia. This document is provided subject to confidentiality obligations of the applicable agreement(s).
This document is intended for use by Nokia’s customers and collaborators only for the purpose for which this document is submitted by Nokia. No part of this document may be reproduced or made available to the public or to any third party in any form or means without the prior written permission of Nokia. This document is to be used by properly trained professional personnel. Any use of the contents in this document is limited strictly to the use(s) specifically created in the applicable agreement(s) under which the document is submitted. The user of this document may voluntarily provide suggestions, comments or other feedback to Nokia in respect of the contents of this document ("Feedback"). Such Feedback may be used in Nokia products and related specifications or other documentation. Accordingly, if the user of this document gives Nokia Feedback on the contents of this document, Nokia may freely use, disclose, reproduce, license, distribute and otherwise commercialize the feedback in any Nokia product, technology, service, specification or other documentation.
Nokia operates a policy of ongoing development. Nokia reserves the right to make changes and improvements to any of the products and/or services described in this document or withdraw this document at any time without prior notice.
The contents of this document are provided "as is". Except as required by applicable law, no warranties of any kind, either express or implied, including, but not limited to, the implied warranties of merchantability and fitness for a particular purpose, are made in relation to the accuracy, reliability or contents of this document. NOKIA SHALL NOT BE RESPONSIBLE IN ANY EVENT FOR ERRORS IN THIS DOCUMENT or for any loss of data or income or any special, incidental, consequential, indirect or direct damages howsoever caused, that might arise from the use of this document or any contents of this document.
This document and the product(s) it describes are protected by copyright according to the applicable laws.
Nokia is a registered trademark of Nokia Corporation. Other product and company names mentioned herein may be trademarks or trade names of their respective owners.